## Slide 1: ERL Sessions
Bettina Kuske and Susan Smith
+
Joint Session Convenors
+
Contributing Speakers

## Slide 2: ERL Sessions Susan Smith & Bettina Kuske
Status and news (4 talks Monday)
Miscellaneous (2 talks & Tom Powers (2))
  inverse Compton scattering of CSR (Compact Linac)
  ERL Cryomodule Development in Japan
Joint with Storage Rings ERLs Vs USR
Joint with Sources I Injectors (4 Talks)
Joint with FELs XFELO (2 Talks)
Limits of Recirculation (2 Talks)
Modelling (3 Talks)
Joint with Sources II Injectors Pulse shaping (2 Talks)
Joint with Sources & Diagnostics Unwanted beam ( 3 Talks)
25 Talks

## Slide 3
ALICE
Susan Smith
Compact ERL
3GeV ERL Light Source
ERLs in Japan
Shogo Sakanaka
BERLinPro
Andreas Jankowiak
JLAB ERL/FELs
Dave Douglas
Status and News

## Slide 4
THz beamline
  ~10s of W @ 0.2 – 1.5 THz
IR FEL
  High power FEL, optics, beam dynamics studies
  14+ kW at 1.6 microns; several kW @ multiple wavelengths
UV FEL
  Recently commissioned (summer 2010)
  High power (100+W) CW 700, 400 nm
  Coherent harmonics into VUV (10 eV)
Now lasing CW again in the IR
DC Gun
SRF Linac
Dump
IR Wiggler
Bunching Chicane
E
f
E
f
E
f
E
f
E
f
E
f
Sextupoles
(B’dL) 10730 G
Sextupoles
(B’dL) 12730 G
Sextupoles
(B’dL) 8730 G
JLab IR Demo Dump
core of beam off center, even though BLMs showed
edges were centered
(high energy tail
JLAB ERL/FELs
Dave Douglas
Machine overhaul, upgrade during next long shutdown

## Slide 5
Characterise in ALICE 2013
ALICE
Susan Smith

## Slide 6
Plan of Laser Compton Scattering Experiment by JAEA
commission cERL, hopefully, in March, 2013

## Slide 7
First beam
21st April 2011
0. 1.8MeV
6pC bunch charge
8kHz (~50nA)
  BESSYVSR
18.3 MV/m
3 x 2-cell Cornell-type
270 kW transmitters
beam through booster envisaged 2015
BERLinPro
Andreas Jankowiak

## Slide 8
Compact ERL
Earthquake proof
ERL SHIELDING @ 100 mA
BERLinPro
Radiation regulatory body proof
BESSY II: 200mC / a @ 1.7GeV typical BERLinPro: some 100mC / 1s @ 50 MeV possible (30kW linac RF-power)

## Slide 9: Miscellaneous

## Slide 10
CSR is reflected at a mirror and
collides with the following electron bunch.
M. Shimada, R. Hajima, PRSTAB 13, 100701, 2010
Miho Shimada: Inverse Compton scattering of CSR（CSR-ICS）
  Optical cavity : Narrow bandwidth. Power amplification by pulse stacking: almost 1000 times.
  Magic mirror : White light with pulse duration of 100 fs.

## Slide 11
Hiroshi Sakai: ERL Cryomodule Development in Japan
INJECTOR
Frequency : 1.3 GHz
Input power : 170 kW CW /coupler
Gradient: 15MV/m
Q0: >1*10^10
Beam current: 100mA (initial 10mA)
All 3 cavities satisfied the cERL requirements with improved HOM couplers
2 cavities (#3, #5) > 25MV/m
#4 cavity up to 20MV/m
Conditioning Results Coupler:
1s, 0.1Hz, 100kW for 2h
cw 30kW for 1.5h
cw 50kW for 0.5h
(ok for 10mA)
cw 100kW for 1 min
Heating inner conductor of warm part
Test with improved cooling soon
LINAC
Frequency : 1.3 GHz
Input power : 20 kW CW /coupler
Gradient: 20MV/m
Q0: >1*10^10
Beam current: 100mA (initial 10mA)
-mode 13.9MV/m
t
Simulation with Fishpact based on Fowler-Nordheim equation
We found the emission source would make the radiation peak at opposite side and also make the radiation peak at other iris point..
Done by E.Cenni
Two cavities reached up to 25MV/m and satisfied cERL requirements of 1*10^10 of Q0 at 15MV/m.
Both cryo modules will be constructed during 2012

## Slide 12: Tom Powers Cost Calculator
Inputs

## Slide 14
Joint session with storage rings:
Christof Steier / Ivan Bazarov: USR versus ERL
Comparison and potential synergies
Benefits of USR has a strong orientation towards typical ERL features: short pulses, high coherence, round beams, flexible operation modes, reduced no. of turns
Special operating modes:
– Single/few-turn, sub-ps bunch mode
– Crab cavity short pulse scheme (shorter bunches plus smaller emittance might allow much shorter pulses compared to SPX)
– 100-1000 turn mode, enabling very low emittance with reduced dynamic aperture, requiring injection of fresh electrons from a superconducting linac operating without
energy recovery (e.g. ~1 mA @ few GeV)
– localized bunch compression systems with components located in long straight sections
– bunch tailoring with low alpha, non linear momentum compaction, multiple RF frequencies
– lasing in an FEL located in a switched bypass, where the post-lasing electron bunches
are returned to the storage ring for damping
– partial lasing at soft X-ray wavelengths using the stored beam, requiring high peak
current created by localized bunch manipulation
USR lattices and optimization procedures become highly complex, but using existing technologies
ERLs just start off and future potentials will develop after ‘generation 1’ goes online

## Slide 15: Joint session:Sources I- Injectors for ERLs
Three areas future collaboration
Emittance and longitudinal bunch properties vs charge
Operating cathode lifetime and integrated charge per cathode intervention
Field emission
  Removal methods (HV, wiping, gas processing & others)
  Characterisation (location, causes etc.)
50 mA record and 35 mA sustainable (Cornell)
Andrew Burrill Requirements and first ideas
Injector development
BERLinPro T. Kamps SRF gun – beam studies with Pb cathode
KEK T. Miyajima DC gun reached > 500kV
JAEA N. Nishimori DC gun reached > 500kV

## Slide 16
Joint session with FEL: XFELO
Shogo Sakanaka: Plans of XFELO in Future ERL Facilities
Ryan R. Lindberg: Overview of XFELO parameters
6 (7) GeV
3GeV ERL
in the first stage
XFEL-O in 2nd stage
lrf/2 path-length
changer
 | XFELO
Beam energy | 7 (6) GeV1)
Beam current | 20 mA
Charge/bunch | 20 pC
Bunch repetition rate | 1 MHz
Normalized beam emittance (in x and y) | 0.2 mm·mrad
Beam energy spread (rms) | 210-4
Bunch length (rms) | 1 ps
Cornell – XFEL-O plans:
7.8 GeV 25m insertion device - or
5GeV with compressed bunches
Lindberg:
Possibilities beyond the canonical K.-J.-Kim parameters
User‘s input needed

## Slide 17: Limits of Recirculation
Effects of Several VLong Undulators
in the APS ERL Design
The impact of undulators in 4GLS
7 GeV, 9 x 48m undulators K=5, 55mm
Energy shift 1.4 MeV noticeable
Use of booster cavities seems advisable
600MeV, 10 m 1 T hel. Undulator
Energy shift 4.6 keV negligible
M. Borland, G. Decker, X. Dong, L. Emery, A. Nassiri,
Proc. PAC09, 44- (2009).
Energy spread increase is fairly modest c.f. CSR increase
Final energy spread of ~1.3 MeV with all gaps closed
No emittance growth seen
Conclusion should be checked with realistic optics errors (i.e., dispersion leaking into straight sections
Negligible emittance growth
Negligible energy spread
CSR in arcs ~1MeV !
Path length change 300fs for long undulator
Use path length chicane seems advisable (feedforward)
Photon pulse lengthening due to long undulator ~ 150 fs, 30fs short
Impact on beam dynamics in general of the varying focussing and non-linear terms was not studied
(http://www.4gls.ac.uk/)
Mike Borland
Jim Clarke

## Slide 18
ALICE Beam Simulations
ALICE in GPT
BC1 Phase
-20deg
-10deg
-5deg
Injector dynamics complicated by reduced gun energy (230 KeV), long multi-cell booster cavity and long transfer line.
Using ASTRA and GPT to go around the machine to understand longitudinal dynamics. Non trivial to use dipoles. GPT (Space charge off) and MAD matching quite good, small differences in vertical focussing.
4.65mm
10mm
Elliptical beam – effect of stray fields?
Bunch-length vs. Linac Phase
Plan to validate 6D machine model to understand different machine set ups with additional diagnostics .
D. Angal-Kalinin
Deepa Angal-Kalinin

## Slide 19
Miho Shimada: Lattice and optics design of both compact ERL and 3-GeV ERL projects
Deceleration
Acceleration
Injection / dump energy: 10 MeV, full energy: 3 GeV
Circumference ~2000 m, linac length : 470 m
22 x 6 m short straight , 6 x 30 m long straight
28 cryo modules, 8 x 9-cell cavities per cryo module
field gradient: 13.4 MV/m, focusing triplets
Deceleration symmetric to the acceleration
Achromatic and isochronous TBA optics in arcs r~20m
1 mm-mrad
5 mm-mrad
9 mm-mrad
enx increases step by step at every each arc.
  In the first inner loop : 1 mm-mrad
  In the outer loop : 5 mm-mrad
The low emittance beam is difficult for 2 loop ERL compared with 1 loop ERL

## Slide 20
Yichao Jing: Bunch compressor design for FEL @ eRHIC
Studies for eRHIC FEL
Choose low energy (~ 10 GeV) for FEL to avoid severe blow up in both emittance and energy spread caused by synchrotron radiation. Normalized emittance assumed to be 0.2 μm in simulation.
Phase space plots show clear evidence of emittance spoil due to the longitudinal – transverse coupling in chicanes.
C-type chicane 1
C-type chicane 2
Opposite bending direction
Smaller bending strength
Phase shifter
Reduction of emittance growth
Promising FEL performance

## Slide 21
Joint session with Sources II: Pulse shaping
Mikhail Krasilnikov: Cathode Laser Pulse Shaping for High Brightness Electron Sources (PITZ Experience)
Core emittance
Electron beam transverse distribution at z=5.74m
Gauss
halo
FlatTop
Reduced halo
Ellipssid
No halo
Significant progress in performance and understanding

## Slide 22
Joint session with Sources II: Pulse shaping
Torsten Quast: Available and Future Pulse Shaping Technologies
 | Difficulty | Quality gain | Stability
transversal I(r) | 3 | ++ | Everybody does it, needs care
Longitudinal I(z) | 7 | + | Good - (feedback control) / 6 examples
spatio-temporal I{r(z)} | 10 | ? | Poor – relying on nonlin. effects
High precision pulse shaper (MBI)
Taken from: Will, Klemz, Optics Express 16 (2008) , 4922-14935
FWHM ~7 ps
FWHM ~ 2 ps
FWHM ~ 24 ps
FWHM ~ 19 ps
FWHM ~ 24 ps
Discussion:
“Is it worth the effort?”
Simple schemes are more reliable and stable
Max. gain is 40% -
but factors of 2 easily lost else where
Benefit depends on application – emittance not unique figure of merit
Blow out regime attractive for
halo reduction
insensitive towards laser parameters

## Slide 23: Joint session with Sources III: Unwanted beam
Five sorts of the unwanted beams
Dynamics: Fraction of the phase space distribution that is far away from the core (due to the beam dynamics), wake fields, resonant HOM excitation
Laser 1: Low charge due to not well attenuated Cathode Laser (ERLs) – but real bunches that have proper timing for acceleration,
Laser 2: Cathode Laser but not properly timed (scattered and reflected light)
Field emission: Dark current or discharges Gun (can be DC or RF), Accelerator itself (can be accelerated in both directions)
RF: microphonics, phase and amplitude instabilities
ELBE J. Teichert Unwanted beam observations at ELBE
PITz M. Krasilnikov Problems observed at PITZ: measurements vs. simulations
JLAB P. Evtushenko Diagnostics Related to the Unwanted Beam

## Slide 24
“The Grand Scheme”
I. Transverse beam profile measurements with Large Dynamic Range
Wire scanner
LDR imaging
CW laser wire
Coronagraph
II. Transverse phase space measurements with LDR
Tomography – where linear optics work (135 MeV)
Scanning slit - space charge dominated beam (9 MeV)
III. Longitudinal phase space with LDR (in injector at 9 MeV)
Time resolving laser wire
(Thomson scattering, CW)
Transverse kicker cavity + spectrometer + LDR imaging
IV. High order optics
to manipulate halo
Drive Laser LDR
measurements
to start modeling with LDR and real
Initial conditions
transverse
longitudinal
cathode Q.E. 2D
V. Beam dynamics modeling with LDR
P. Evtushenko

## Slide 25: Problems observed at PITZ: measurements vs. simulations
1nC
0.1nC
Mikhail Krasilnikov

## Slide 26
assuming an unwanted beam of < 1 µA in CW accelerators with SRF guns
there will be a need for photo cathodes with low dark current
proper handling to prevent dust particles and damage
plug materials and roughness
photo layer properties
- roughness, homogeneity, thickness
- high work function
- crystal size and structure
- multi-layer design
- post-preparation treatment (ions, heating)
- pre-conditioning
20% Cathode (80% scratch on cavity)
courtesy of
F. Obier/DESY
Dark current kicker
Pulsed operation
bunch 100 pC
dark current at 1.3 GHz
100 ms
10 ms
pulsed RF
laser
10 ms
Unwanted Beam Observations at ELBE
J. Teichert