## Slide 1: Digitization System R&D for APV25
Xinglong Li
China Institute of Atomic Energy
(中国原子能科学研究院)

## Slide 2: Outline
Introduction
System construction
Results
Next step

## Slide 3: Introduction
-> APV25
· 128 channel pre-amplification
· 192 cell pipeline
· a single analogue differential output
-> Objective
Develop a system to control APV25 , digitize and save the APV25 output .
SRS
MPD
MRS
-> Similar system existing
· SRS (scalable readout system) @RD51 -developed
· MPD (Multi Purpose Digitizer) @INFN - developed
· MRS (Multiple-chip Readout System) @USTC -developing
· ...

## Slide 4: Outline
Introduction
System construction
Results
Next step

## Slide 5: System construction
APV25
ADC
FPGA
PC
Analogue data
Clock, Trigger, Cmd
Digital data
Parameters
GbE
HDMI
ADS5242
Spartan 6
APV25 backplane
HDMI
GbE
power
power

## Slide 6: APV25 details
APV25
ADC
FPGA
PC
Analogue data
Clock, Trigger, Cmd
Digital data
Parameters
GbE
HDMI
Preamplifier
Shaper
Buffer
APSP
128:1 Multiplexer
Preamplifier
Shaper
Buffer
APSP
Preamplifier
Shaper
Buffer
APSP
Preamplifier
Shaper
Buffer
APSP
. . . . . . .
1
2
3
. . . . . . .
128
Channel
Clock
Trigger
Command(I2C)
Analogue data

## Slide 7: ADC details
APV25
ADC
FPGA
PC
Analogue data
Clock, Trigger, Cmd
Digital data
Parameters
GbE
HDMI
Analogue data
ADS5242
4-Channel
12-Bit
65MSPS
Analog-to-Digital Converter
Clock
Command
Serial digital data

## Slide 8: FPGA details
APV25
ADC
FPGA
PC
Analogue data
Clock, Trigger, Cmd
Digital data
Parameters
GbE
HDMI
Serial digital data
ISERDES2
Serial to parallel
FIFO
GbE MAC
(UDP)
RTL8211E
PHY
Gigabit Ethernet cable
Clock
I2C
ADC Ctrl
To ADC & APV25
Spartan 6
FPGA utilization: 50% BUFG, 22% IO, ≤ 10% others

## Slide 9: PC details
APV25
ADC
FPGA
PC
Analogue data
Clock, Trigger, Cmd
Digital data
Parameters
GbE
HDMI
GbE
cable
LabVIEW program
C program based on SOCKET API
SOCKET sendto
SOCKET recvfrom
binary file
UDP send
UDP receive
Datagram
to data
Waveform

## Slide 10: Outline
Introduction
System construction
Results
Next step

## Slide 11: APV25 data received (LabVIEW)
Jones, L. L., et al. "The APV25 deep submicron readout chip for CMS detectors." (1999).
header, addr, error
Signal injected
ticks
Signal of 1~128 channel

## Slide 12: Gigabit Ethernet speed test(SOCKET)
The UDP function of LabVIEW is slower…
-> UDP protocol with Cumulative acknowledgment
(1 ACK every 10 datagram)
Send ACK | 14%
Receive datagram | 62%
Write to file | 24%
-> 731 second, 108 datagrams, no lost, 40GB file (on SSD) ,
i.e. 460Mb/s
-> Time cost:

## Slide 13: Outline
Introduction
System construction
Results
Next step

## Slide 14: Next step
FPGA
  Add zero compression to reduce data rates to the computer.
  Add Retransmission timeout to make the transmission more reliable.
LabVIEW program
  Use SOCKET API or other similar API instead of the slow UDP function.
  Improve data processing and save the results.
New version system
  Design FPGA board instead of the development board.
  Digitize 8 or 16 APV25 in 1 system.

## Slide 15: Thank you!