## Slide 1
Progress of GEM R&D in Lanzhou University
Hui-Yin Wu(吴会寅)

## Slide 2
Outline
Jul. 27, 2017 Progress of GEM R&D in LZU 2
Time properties of GEM-detector signal
Position correction
R&D of GEM-DAQ
Future plan

## Slide 3
Time properties of GEM-detector signal
Jul. 27, 2017 Progress of GEM R&D in LZU 3
+
+
+
+
+
+
+
+
Readout PCB
Center of gravity
Point of incidence
ΔX
α
+
+
+
+
+
+
+
Cathode
+
+
+
Work Gas
Point of incidence
A typical GEM detector: Cathode; Drift region; GEM foils; Induction region; Readout PCB

## Slide 4
Jul. 27, 2017 Progress of GEM R&D in LZU 4
Time properties of GEM-detector signal
The velocity of Alpha (~7mm/ns) is much larger than the drift velocity of electron(~0.05mm/ns)

## Slide 5
Jul. 27, 2017 Progress of GEM R&D in LZU 5
Position correction
45°
100um thick FR4 can completely block Alpha particle.
Alpha particle can incident at 45° at most.
Cathode is made of a 2um Aluminized Mylar foil reducing to block Alpha particle energy.

## Slide 6
Jul. 27, 2017 Progress of GEM R&D in LZU 6
Position correction
Slit
Detector
THGEM foil: a thickness of 200 um, pitch of 600 um, a hole diameter of 200 um, and a rim of 80 um
APV25 chip with 25ns sample period
Strip readout with pitch of 600 um

## Slide 7
Jul. 27, 2017 Progress of GEM R&D in LZU 7
Position correction
A typical Alpha signal with 6 samples(maximum number of samples：MPD) The center of gravity shift to the right along with time increase.

## Slide 8
Jul. 27, 2017 Progress of GEM R&D in LZU 8
Position correction
α
1st sample
2nd sample
3rd sample
4th sample
5th sample
6th sample
+
+
+
+
+
+
L1
L2
S1
S2
L1/L2=S1/S2=A
…
Similar triangle problem

## Slide 9
Jul. 27, 2017 Progress of GEM R&D in LZU 9
Position correction
t=a*p + b (2)
Y=a*X+ b (1)
Each event go
through (p, t)
a and b represent the linear fitting parameters for each track.

## Slide 10
Jul. 27, 2017 Progress of GEM R&D in LZU 10
Position correction
Linear Fit gravity center of first three samples for each track and get the parameters a and b

## Slide 11
Jul. 27, 2017 Progress of GEM R&D in LZU 11
Position correction
Before correction
After correction
2056
645
137.28
137.40
FWHM
MAIN
Channel=b-x*a
a and b are linear fitting parameters for each track
x=-15.36.3

## Slide 12
Jul. 27, 2017 Progress of GEM R&D in LZU 12
Connect to Readout PCB: 140P signal + 18P Ground
Connect to APV25 signal input
Connect to APV25 Ground
R&D of GEM-DAQ
4 layers PCB with
2 Ground layers

## Slide 13
Jul. 27, 2017 Progress of GEM R&D in LZU 13
R&D of GEM-DAQ

## Slide 14
Jul. 27, 2017 Progress of GEM R&D in LZU 14
R&D of GEM-DAQ
New DAQ Unit
Control Output
HDMI A 19Pins
Signal Input
HDMI A19Pins
Trigger Input
LED
Ethernet Port
One unit can control 16 APV25 chips, total 2048 Channels.
30 samples per event
FPGA: Xilinx-V5

## Slide 15
Jul. 27, 2017 Progress of GEM R&D in LZU 15
R&D of GEM-DAQ
New backplane
4 Apv25 chips per backplane
1
2
3
4
New
DAQ
HDMI A

## Slide 16
Jul. 27, 2017 Progress of GEM R&D in LZU 16
Future plan
Develop the new DAQ system
Try to correct position in FPGA chip(online)

## Slide 17
Jul. 27, 2017 Progress of GEM R&D in LZU 17
Thank you for your attention