## Slide 1: Recent Results of PandaX Dark Matter Searching Experiment
Changbo Fu
Shanghai Jiao Tong University
On Behalf of Collaboration
27July2017

## Slide 2: Outline
Introduciton
  Dark Matter: WIMPs, Axion, …
  PandaX at China Jinping Underground Lab（CJPL)
Operation and Data Analysis
  Calibration
    Energy/Position Calibration
    Electrical Recoil (ER) and Nuclear Recoil (NR)
  Radiation Background Analysis
    85Kr, 137Xe…
  Results: WIMPs (Spin-indep. and Spin-dep.)
  Results: Axion (preliminary)
Summary and Future Plan
  Operation of PandaX-I&II
  Upgrade: PandaX-IV (4-ton Detector)
  Upgrade: PandaX-III (136Xe 0vbb)

## Slide 3: The Mass in Our Universe
Dark matter 26.8%
  WIMP?
  Axion?
  Dark Photon?
  …
Dark energy 68.3%
4.9%
？
？
Ordinary matter

## Slide 4: WIMP? Axion? …
1977, Peccei-Quinn Sym.
If the Symmetry breaks
----> Axion
Good Theoretical Solution
Good dark matter candidate
WIMP
May freeze out early as universe cooling down
Extremely small CS with normal matter
Spin-Dependent or not?
Notes: Lambda range, window

## Slide 5: China JinPing Underground Laboratory (CJPL-I)
2400m
8000m
锦屏山
Deepest in the world ( 1µ/week/m2) and Horizontal access!

## Slide 6: From CJPL-I  CJPL-II
Exp. Halls
Headrace Tunnels
Traffic Tunnels

## Slide 7: PandaX: a Dual-phase Xe TPC
Energy: Photon(S1)+e(S2)
Position: XYZ(light pattern+TOF)
PID: S1/S2
  ER: photon, Axion, Dark Photon…
  NR: neutron, WIMP, …
dT

## Slide 8: PandaX @ CJPL-I&II
PandaX-I: 120 kg DM experiment
2009-2014
PandaX-II: 500 kg DM experiment
2014-2018
PandaX-III: 200 kg to 1 ton HP gas 136Xe 0vDBD experiment
Future
PandaX-xT: multi-ton (~4-T) DM experiment
Future
＝Particle and Astrophysical Xenon Experiments
CJPL-I
CJPL-II
Notes: The first such experiment I am going to discuss is PandaX, that I work on. This experiment had a rather late start since 2009, but ramped up very quickly. Up-to-now, we have two phases developed in CJPL. The 2nd phase is running with 500-kg active target. In the future, PandaX will also move to the new CJPL-II to perform multi-ton DM experiment (we call it xT for now), as well as ton-scale 136Xe 0vDBD experiment, named PandaX-III.

## Slide 9: PandaX-II Running History
Enginnering Running： from the beginning of 2015, Fix various problems
Commissioning Run I(Run8)： 2015.11. 22 – 12.14 (19.1days 306kg， FV) with high Kr background (Phys. Rev. D. 39, 122009 (2016))
Commissioning Run II (Run9)：First Low background Running, re-distillation to remove Kr, 2016.03.09-06.30 (79.6 days) PhysRevLett.117.121303
Running Now smoothly at this moment!

## Slide 10: PandaX-II, New Features
More than Large Volume
New IV: inner vessel with clean Low Rad. SS
New PMTs: 55+55, 3” High Quam Eff., improved base design (±650V).
New Veto PMTs in skin
New OC: overflow chamber at Bottom, save expensive Xenon
Better Reflector: Improved Reflectivity

## Slide 11: Electron Lifetime
2015.11.22---12.14
2016.03.09---06.30

## Slide 12: Calibration Program
Electrical Recoil（ER）
  Internal/external ER peaks:
    Detector uniformity corrections
    Light/charge collection parameters
  CH3T injection: tritium beta decays
    Simulate ER background
Nuclear Recoil（NR）
  Low rate AmBe neutron source:
    Simulate DM NR signal
Energy Cali.
Position Cali
ER/NR Cali.

## Slide 13: ER cal. w/ CH3T β source
18.0 hours of tritium data taken, with ~2800 low energy ER events collected
9 events leaked below NR median, (0.32+/-0.11)%
Consistent with Gaussian expectation
Following method from PRD93 (2016)072009

## Slide 14: Nuclear Recoil (NR) calibration
162.4 hours of AmBe data taken, with ~3400 low energy single scatter NR events collected
NR median curve and NR detection efficiency determined

## Slide 15: Radiation Background
ER background
  85Kr (suppressed by a factor 10)
  127Xe (due to surface exposure of Xe during distillation)
  Others: U/Th/Rn…
  Accidental background (determined by data)

## Slide 16: Radioactive background: 85Kr in Xe
Kr-85, T1/2=10.756 y, Beta Emax=687 keV
Journal of Instrumentation 11/2014; 9:11024

## Slide 17: 85Kr Indentified by the TPC
Identified by delayed b-g coincidence analysis
Uniform distribution
Significantly reduced after distillation
Waveform: one b
one g
85Kr
85Rb (stable)
β1(0.437%)
β2(96.563%)
γ1(514KeV)
10.73y

## Slide 18: 127Xe
127Xe (408 keV)
127Xe/129mXe
Fitted half-life: 33.3 day (expected 36.4 day)
Average 127Xe rate in the low energy DM search region (<10 keV) estimated to be 0.42±0.10 mDRU (DRU = evt/kg/keV/day)
128,129Xe(ɣ, xn)127Xe

## Slide 19: Major Radiation Background

## Slide 20: Final selection cuts
    Volume Cut (FV in Run 9 with 328.9 kg)
  Horizontal cut determined by distribution of events with S1 between [45,200] PE and suppressed S2
  Vertical cut: Upper boundary consistent with the previous analysis; Lower boundary determined by X-events from 127Xe MC
Threshold
  S1 cut:[3,45] PE
  S2 cut[100raw, 10000]PE

## Slide 21: Final WIMP candidates (run 8&9)
99.9% NR acceptance
100 PE S2 cut
Run9
ER median
NR median
99.9% NR acceptance
100 PE S2 cut
Run8
ER median
NR median
Total exposure:
33,000 kg-day

## Slide 22: Searching Results: WIMPs (Spin-Indep.)
Phys. Rev. Lett. 117, 121303 (2016)
2.5x10-46 cm2
1-σ band
2-σ band
Notes: Phys. Rev. Lett. 117, 121303 (2016)

## Slide 23: Results: WIMPs (Spin-dep.)
Phys. Rev. Lett. 118, 071301 (2017)

## Slide 24: Data Set for Axion Searching
Almost the same data set as WIMP-search case, but E extended to 25keV

## Slide 25: Solar Axion Sources
Compton-like scattering (C)
Axion-bremsstrahlung (B),
Atomic-recombination (R),
Atomic-deexcitation(D)
E. Armengaud, et al., J. Cosmol. Astropart. Phys. 2013, 067 (2013).

## Slide 26: Searching Results: Solar Axion (Preliminary)

## Slide 27: Galactic ALP Sources
Milky Way Dark Matter
  on the Earth location
Detecting Rate by something like Xe
J. Cosmol. Astropart. Phys. 2013, 067 (2013)
Phys. Rev. D 78, 115012 (2008)

## Slide 28: Searching Results: (Preliminary) Galactic Axion-Like Particles

## Slide 29: PandaX ---- in Future
PandaX-I: 120 kg DM experiment
2009-2014
PandaX-II: 500 kg DM experiment
2014-2018
PandaX-III: 200 kg to 1 ton HP gas 136Xe 0vDBD experiment
Future
PandaX-xT: multi-ton (~4-T) DM experiment
Future
CJPL-I
CJPL-II
Notes: The first such experiment I am going to discuss is PandaX, that I work on. This experiment had a rather late start since 2009, but ramped up very quickly. Up-to-now, we have two phases developed in CJPL. The 2nd phase is running with 500-kg active target. In the future, PandaX will also move to the new CJPL-II to perform multi-ton DM experiment (we call it xT for now), as well as ton-scale 136Xe 0vDBD experiment, named PandaX-III.

## Slide 30: The New Exp. Hall, CJPL-II
The Cave
The Water Pool
13m

## Slide 31: PandaX Upgrading
Water Shielding
  5000Ton pure water
  U/Th <10-14 g/g
Rn ctrl.
  <1mBq/m3 in water;
  ~10Bq/m3 in the cave
Fresh air

## Slide 32: PandaX-III&IV Modules
150Kg 136Xe (90%)
PandaX-III(0vbb)
  Better E Res. than liquid
  Position Sensitive
PandaX-4T
  6ton total, 4ton sensitive target
  2019—2020 on-site assembling

## Slide 33: Summary
Using data from PandaX-II (500kg) 79.6+19.1 days data， ~33,000 kg-day exposure, No WIMP was found.
  Limits on SD and SI WIMP-nucleon cross sections were obtained.
Using data from PandaX-II (500kg) 79.6 days data， ~27,000 kg-day exposure, No Solar or Galactic ALP was found.
  For Solar Axion, we set constraints, including 57Fe (preliminary).
  For Galactic ALP, we set constraints in axion mass range about [1, 10]keV (preliminary).
We are under preparation to the future PandaX-4T program.
We are working on 136Xe 0vbb.

## Slide 34: PandaX Collaboration
Shanghai Jiao Tong U (2009-)
Peking U (2009-)
Shandong U (2009-)
Shanghai Inst. App Phys, CAS (2009-)
U of Science & Tech. (2015-)
China Inst. of Atomic Energy (2015-)
Sun Yat-Sen U (2015-）
Yalong Hydropower (2009-)
U of Maryland (2009-)
U of Michigan (2011-2015)
Alt Eng. & Atom Eng. Comm. (2015-)
U of Zaragoza(2015-)
Suranaree U of Tech. (2015-)

## Slide 36: Extracting Det. Parameters
W = 13.7 eV
PDE: Photon Det Eff.
EEE: Electron Extr. Eff.
SEG: Single Electron Gain.
SEG  Determined by identifying Single Electron Events.
PDE/EEE  One Eq.; Two Variables

## Slide 37: PandaX Detector System
PandaX
Xe TPC
LowTemp
Vacuum
Pre-
Distillation
Online
Purify
Electronic
Radiation
Control