MOM Update
Controls & Monitoring
in
MICE
Pierrick Hanlet
 28 February 2011

---
Controls & Monitoring
Purpose:
Controls refers to:
user interface to equipment
proper sequencing of equipment
Monitoring serves to:
protect equipment (early notification)
protect data quality

---
Controls & Monitoring
MICE is a precision experiment
Guiding principle: control, or at least measure, systematic uncertainties
Monitoring must be performed on all parameters affecting data quality:
Example – ToF system has 50ps resolution
DT -> cable expansion -> cable inductance -> time error

---
Present Organization
Task divided into multiple systems:
Beamline:
Target, magnets, PA, DS, BS, Diffuser
Particle ID
LM,TOF, CKOV, BPM, KL, EMR
Environment monitoring
T, Humidity, radiation, water, He, ...
DAQ
DAQ—CDB—C&M interface, crates,network, ...

---
Present Organization
Task divided into multiple systems:
Tracking
tracker and spectrometer solenoids
AFC
absorber and focusing coils
RFCC
RF cavities and coupling coils

---
Future Organization
Task divided into multiple systems:
Beamline:
Target, magnets, PA, DS, BS, Diffuser
Particle ID
LM,TOF, CKOV, BPM, KL, EMR
Environment monitoring
T, Humidity, radiation, water, He, ...
DAQ
DAQ—CDB—C&M interface, crates,network, ...
This is all part of Step I

---
Future Organization
Task divided into multiple systems:
Tracking
tracker and spectrometer solenoids
AFC
absorber and focusing coils
RFCC
RF cavities and coupling coils
Steps II & III
Steps II & III
Step IV
Step V

---
Future Organization
But we're not done with the planning: a major consideration is not yet in place!
Over arching control of C&M and DAQ with state machines defining MICE

---
MICE State Machines
Several Considerations:
Subsystem C&M developed by different collaborators
Must be integrated to ensure safe use of resources and operations
MICE operates in different states over differing time periods:
Shutdown/Installation
Sleep (occasionally over weekends)
Testing
Data taking

---
MICE State Machines
Different states requires different equipment (and data) monitoring requirements:
ignore many systems during shutdown state
fewer systems ignored during sleep state
nothing(?) ignored during data taking
different parameters during testing or data taking?
different alarms and different alarm limits
different parameters and/or frequency to archive

---
MICE State Machines
MICE Configuration Database is the “memory” of the experiment.
All parameters stored in CDB
All parameters referenced from CDB (reduce human error)
Different configurations, “states”:
Must be defined
Must be “tagged” in the CDB

---
MICE Run Sequence
Step IV Example (10,240) run:
Start run will require:
Set magnet currents
Set DS currents
Set PA
Set diffuser
Set cooling channel magnets
Absorber settings
Verify tracker ready
Verify BS, DAQ, network ready
Check hall environment
Start DAQ
All from CDB

---
Status
Step I C&M components operational
Step IV plan underway
Cooling channel magnets will have uniform C&M
Over-arching plan taking shape
CDB designed and built
Interface functionality being developed

---
Summary
New systems come online and are (mostly) accounted for
Integration for new systems requires proper planning