## Slide 1: Muon Capture for a Muon Collider
David Neuffer
July 2009

## Slide 2: 0utline
Motivation
  μ+-μ- Collider front end
Produce, collect and cool as many muons as possible
    Start with ν-Factory IDS design study
  Reoptimize for Collider
    Shorter bunch train
      Higher energy capture, shorter front-end
    Larger gradients
Beam Loss problem
  Chicane, Absorber, shielding
Discussion

## Slide 3: Muon Collider/NF Beam Preparation
Baseline Muon Collider beam preparation system similar to that for Neutrino Factory
  downstream portions (6D cooling, acceleration, collider) are distinct
    much more cooling and acceleration needed for collider
Neutrino Factory
Muon Collider

## Slide 4: IDS Baseline Buncher and φ-E Rotator
Drift (π→μ)
“Adiabatically” bunch beam first (weak 320 to 232 MHz rf)
  P0 = 233; PN=154 MeV/c N=10
Φ-E rotate bunches – align bunches to ~equal energies
  232 to 2022 MHz, 12MV/m
Cool beam 201.25MHz
18.9 m
~60.7 m
FE Target
Solenoid
Drift
Buncher
Rotator
Cooler
~33m
42 m
~80 m
p
π→μ

## Slide 5: Neutrino Factory version
NF baseline version
  Captures both µ+ and µ-
  ~0.1 µ/p within IDS acceptance
    εT < 0.03, εL < 0.15
Basis for cost/design studies
  rf requirements
  Magnet requirements
23 bunches
0m
Drift - 80m
Bunch-110m
Rotate-150m
Cool-240m
700 MeV/c
0 MeV/c
-30m
30m
v

## Slide 6: Rf Buncher/Rotator/Cooler requirements
Buncher
  37 cavities (13 frequencies)
  13 power supplies (~1—3MW)
RF Rotator
  56 cavities (15 frequencies)
  12 MV/m, 0.5m
  ~2.5MW (peak power) per cavity
Cooling System – 201.25 MHz
  100 0.5m cavities (75m cooler), 15MV/m
  ~4MW /cavity
Front End section | Length | #rf cavities | frequencies | # of freq. | rf gradient | rf peak power requirements
Buncher | 33m | 37 | 319.6 to 233.6 | 13 | 4 to 7.5 | ~1 to 3.5 MW/freq.
Rotator | 42m | 56 | 230.2 to 202.3 | 15 | 12 | ~2.5MW/cavity
Cooler | 75m | 100 | 201.25MHz | 1 | 15 MV/m | ~4MW/cavity
Total drift) | ~240m | 193 |  | 29 | ~1000MV | ~550MW
Magnet Requirements:
rf

## Slide 7: Rf cavity
Concept design construction operation

## Slide 8: Toward Muon Collider
Bunch trains for NF - ~80m
  Best 23 bunches (~35m) have ~75% of captured muons
Rf within magnetic field problem must be solved
  Pill box rf baseline
  Magnetic insulation
  Bucked-coil
  Gas-filled rf
Assume will be solved
  µ+µ- Collider will improve to the next level of performance

## Slide 9: Reoptimize for µ+µ- Collider Front End
Muon Collider front end optimum is somewhat different
  Short bunch train preferred
    Bunches are recombined later …
  Maximum μ/bunch wanted
  Longitudinal cooling included; may accept larger δp
  Larger rf gradient can be used (?)
    NF will debug gradient limits
    Cost is less constrained
For variant, we will have shorter BR system, more gradient, and capture at higher momentum
  230  275 MeV/c
  150m  120m
  9/12/15 MV/m  12.5/15/18 or 15/18/20 MV/m
  1.5T2T

## Slide 10: High-frequency Buncher and φ-E Rotator
Drift (π→μ)
“Adiabatically” bunch beam first (weak 350 to 232 MHz rf)
  P0 = 280; PN=154 MeV/c N=10
Φ-E rotate bunches – align bunches to ~equal energies
  232 to 202 MHz, 15MV/m
Cool beam 201.25MHz
  1.2cm Li H, 15 MV/m
Similar to Neutrino Factory
18.9 m
~40m
FE Target
Solenoid
Drift
Buncher
Rotator
Cooler
~33m
34 m
~80 m
p
π→μ

## Slide 11: Rotated version
End up with fewer, larger N, bunches
  More μ/p ~
    20-40% more ??
  Larger δp (larger εL/bunch)
15 bunches

## Slide 12: Collider version
Has ~30% shorter train
More μ/p
  ~0.15 μ/p (from ~0.11)
Captures more of the “core” of the initial π/μ
  Rather than lower half of the core …
0
1.0 GeV/c
IDS
NEW MC
All at target

## Slide 13: Further iteration?
ΔN: 108
Rf gradients: 12.5  15  18 MV/m
  Or 15  18  20 MV/m
Shorter system ~102m
14.05 m
~33m
FE Target
Solenoid
Drift
Buncher
Rotator
Cooler
~25.5m
27 m
~80 m
p
π→μ

## Slide 14: N=8 variant
Chart: 
0
800 MeV/c
εL/10
εT
Shorter bunch train
  But not that much
    15  12 bunches
  Bunch phase space larger
  Longitudinal cooling ?
0.2
0.3
µ-/p

## Slide 15: Beam losses along Front End – half-full?
Start with 4MW protons
  End with ~50kW μ+ + μ-
    plus p, e, π, …
    ~20W/m μ-decay
  ~0.5MW losses along transport
    >0.1MW at z>50m
“Hands-on” low radiation areas if hadronic losses < 1W/m
  Booster, PSR criteria
  Simulation has >~100W/m
    With no collimation, shielding, absorber strategy
Need more shielding, collimation, absorbers
  Reduce uncontrolled losses
  Special handling
Drift
Cool

## Slide 16: Comments on Front End Losses
First ~70m has 30cm beam pipe within ~65cm radius coils
  ~30+ cm for shielding
  Radiation that penetrates shielding is what counts …
    < 1W/m ?
  Could the shielding handle most of the losses in the first ~70m?
Major source is protons
Shielding ?
12.7 m
~60.0 m
FE Target
Solenoid
Drift
Buncher
Rotator
Cooler
~33m
42 m
~90 m
p
π→μ
Protons after target

## Slide 17: Comments on Losses
Other than protons, most losses are μ’s and e’s from μ-decay
  Less dangerous in terms of activation
    > 1W/m OK ?
  μ’s would penetrate through more shielding
High energy Protons (>4GeV) do not propagate far
  8 GeV lost in Beam dump
Large spectrum at lower energies
  ~20kW; 1GeV protons
  significant number propagate down cooling channel
  Losses at absorbers
Some protons captured in “cooling rf buckets”
  ~30/10000
  2GeV p

## Slide 18: Chicane to remove high-energy p
C Rogers ( see also Gallardo/Kirk) suggests using Chicane to filter out unwanted p/e/
  Sample parameters
    5m segments-10 coils 1.25/coil
    Larger momenta >400─500 MeV/c not accepted

## Slide 19: Chicane removes high-energy particles
Single chicane works as well as double chicane (?)
  Offsets orbit
Works for both signs
Would remove most hadronic residual
  Heats beam? <10% ?
But must absorb losses somehow …

## Slide 20: Chicane Performance

## Slide 21: Parameters of Proton Absorber
Absorbers reduce number of protons
  Losses occur near absorber
  Significant proton power remains
10cm C = 40MeV
Tried 1 to 4 cm Be
  Similar localized losses
  Less perturbation to cooling system

## Slide 22: Comments
Muon Collider version is an incremental change from IDS
  ~25 to 33% shorter
  Higher gradients
    9/12/15  15/16/18 ?
  Capture at ~275MeV/c rather than 230MeV/c
Collider optimum might be a further increment along … ?
Optimization should include initial cooling with 6-D
  Used only transverse in present study, LiH absorbers (~1.2cm)

## Slide 23: Summary
Muon Accelerator Program