## Slide 1: Practical design of helical cooling channel
Katsuya Yonehara
APC, Fermilab

## Slide 2: Outline
Show result of 200 MHz base HCC simulation by using analytical electromagnetic field
  To demonstrate cooling efficiency and compare with other cooling channels
Show beam & lattice parameter list
  To find out what is critical parts in channel
No cost estimation of HCC made yet but made some practical design of beam elements
  Demonstrate tolerance of helical solenoid (HS) coil
  Estimate RF power dissipation and possible cryogenics
  Possible RF cavity to incorporate into the HS magnet

## Slide 3: Helical Cooling Channel
No periodic structure ⇒ Large beam phase space

## Slide 4: 200 MHz base HCC
PIC=Parametric resonance Ionization Cooling channel
REMEX=Reverse EMittance EXchange channel
Analytical Electromagnetic field

## Slide 5: Cooling efficiency in 200 MHz base HCC
Use analytical Electromagnetic field
There is an RF window between two
RF cavities
0.12, 0.08, 0.06 mm thick Be window
in 200, 400, and 800 MHz HCCs,
respectively
GH2 pressure = 160 atm @ STP
Phase space matching between two
helices is NOT optimized
Main beam loss mechanism is due to
mismatching in longitudinal phase space
Nevertheless, we observe similar cooling
performance as in 325 MHz base HCC
(see backup slide)

## Slide 6: Parameter list
 | Z | b | b’ | bz | ν | E | κ | λ | εμ | εT | εL | ε6D
unit | m | T | T/m | T | GHz | MV/m |  | m |  | mm rad | mm | mm3
 | Channel length | @ ref | @ ref | @ ref | RF |  | p⊥/pz |  | Trans- mission | RMS normalized |  | 
0 |  |  |  |  |  |  |  |  | 1.0 | 21 | 23 | 8900
1 | 100 | 1.2 | -0.21 | -4.2 | 0.2 | 16 | 1.0 | 1.0 | 0.75 | 1.9 | 4.3 | 9.4
2 | 91 | 1.8 | -0.42 | -6.0 | 0.4 | 16 | 1.0 | 0.7 | 0.62 | 0.86 | 1.8 | 0.99
3 | 86 | 3.1 | -1.29 | -10.7 | 0.8 | 16 | 1.0 | 0.4 | 0.41 | 0.32 | 1.0 | 0.08
4 | 24 | 4.2 | -2.29 | -14.0 | 0.8 | 16 | 1.0 | 0.3 | 0.38 | 0.34 | 1.1 | 0.07

## Slide 7: Estimate RF parameter
 | Z | κ | λ | ν | E | Lcavity | Rcavity | Dissipation Ppeak | Stored E | Dissipation Pave
unit | m |  | m | GHz | MV/m | cm | cm | MW/m | J/m | kW/m
 | Channel length |  |  | RF |  | 10 cavities/λ |  |  |  | Rep rate = 15 Hz
0 |  |  |  |  |  |  |  |  |  | 
1 | 100 | 1.0 | 1.0 | 0.2 | 16 | 10 | 57.1 | 43.3 | 313 | 17.9
2 | 91 | 1.0 | 0.7 | 0.4 | 16 | 7 | 28.6 | 23.2 | 78.2 | 3.4
3 | 86 | 1.0 | 0.4 | 0.8 | 16 | 4 | 14.3 | 14.7 | 19.5 | 0.76
4 | 24 | 1.0 | 0.3 | 0.8 | 16 | 3 | 14.3 | 18.5 | 19.5 | 0.95
Based on NRF (Cu, σ=5.8×108 mho/m@room temperature) pillbox cavity
Total Pave: 2.2 MW

## Slide 8: Tolerance of helical solenoid magnet
α
β
Longitudinal spacial
occupancy rate = β/α
30.0 %
37.5 %
50.0 %
15.0 %
22.5 %
Tolerance in longitudinal direction
Tolerance in transverse direction
HS coil radius
dependence
HS coil position
(r offset from
magnet center)
dependence
Chromaticity curve
No change up to 30 %
70 % of space will be used
for infrastructure
HS coil has a better cooling performance than analytical field
because of better uniformity of field
Transverse geometry study suggests
optimum HS coil shape may not be a circle

## Slide 9: RF cavity in HS magnet
Dielectric loaded RF
Re-entrant RF
Chart: Loss Tangent of Alumina Ceramics as a function of temperature
| 300.0 | 200.0 | 100.0 | 70.0 | 50.0
sapphire | 1e-05 | 6e-06 | 5e-07 | 1e-07 | 3e-08
WESGO "warm" | 0.00021 | 4.6e-05
Friatec "warm" | 0.00047 | 6e-05
WESGO "cold" | 0.00048 | 4.4e-05

Q77K ~ 20,000 for full ceramic loaded cavity
Optimization (shape, material, etc) is needed
HS coil will be located in the nose cone
Practical helical RF cavity will be
combined both concepts

## Slide 10: Cryogenic operation
Merit
Low pressure gas wall
High conductivity RF
  Less RF power dissipation
  Less peak power
  Ex) Reduction factor 4.5 @ 77 K
Low loss tangent
Less temperature difference between RF cavity and SC magnet
Disadvantage
Complicate & more cost
State of many materials are liquid or solid at low temperature (limit on the species of dopant gas)
Possible temperature range
55 Kelvin: Oxygen melting point < T < 80 Kelvin LN2 @ 1 atm

## Slide 11: Compare RF power consumption in 200 and 325 MHz base HCCs
ν | E | Lcavity | Rcavity | Dissipation Ppeak | Stored E | Dissipation Pave
GHz | MV/m | cm | cm | MW/m | J/m | kW/m
RF |  | 10 cavities/λ |  |  |  | Rep rate = 15 Hz
0.2 | 16 | 10 | 57.1 | 43.3 | 313 | 17.9
0.4 | 16 | 7 | 28.6 | 23.2 | 78.2 | 3.4
0.8 | 16 | 4 | 14.3 | 14.7 | 19.5 | 0.76
0.325 | 27 | 10 | 35.3 | 65.4 | 341 | 13.1
0.65 | 27 | 7 | 17.7 | 36.0 | 85.2 | 2.6
1.3 | 27 | 4 | 8.8 | 23.2 | 21.3 | 0.58
In STP condition
Tried to find 20 kW/m @ 77 Kelvin of cooling power
Need a special cooling system

## Slide 12: Force flow LN2 cooling system
LN2 chiller
& circulator
Cryo RF
system
LN2 inlet (66 K)
LN2 outlet (70 K)
m: LiN2 flow rate m3/s
c: Specific heat 2019 J/K/kg
ΔT: Temperature difference
(TLN2 from 66.4 to 77 K)
ρ: Density 853 kg/m3
m ~ 3 Litters/s @ΔT = 4K
Cooling efficiency of chiller: ~10 %

## Slide 13: Study matching section
Baseline design of matching section (transport beam from coaxial straight to helical structure) has been made
Change HS coil center position adiabatically
Tune longitudinal beta oscillation by changing the length of section and the current density of HS coil
Almost 100 % transmission
Longitudinal phase space grows
This can be fixed by putting RF cavity in the section
Or tune phase slip factor
Include pressure window effect in future study

## Slide 14: Fill high pressurized gaseous hydrogen in RF cavity
GH2 is one of the best ionization cooling absorber
GH2 is a buffer gas to suppress the breakdown
In fact, high pressure GH2 filled cavity is insensitive with B field
GH2 is a good coolant to keep temperature of cavity and RF window
Need more tests
Beam loading effect with intense beam

## Slide 15: Working group
Original inventors & analytic investigation
Yaroslav Derbenev, Rolland Johnson
For homogeneous absorber filled HCC
Simulation tool developer
Tom Roberts, Rick Fernow
Developer in simulation
Alex Bogacz, Kevin Beard, Katsuya Yonehara
Kevin Paul, Cary Yoshikawa, Valeri Balbekov, Dave Neuffer
Developer of beam elements
RF: Mike Neubauer, Gennady Romanov, Milorad Popovic, Alvin Tollestrup,
Al Moretti, Moses Chung, Andreas Jansson
Magnet: Gene Flanagan, Steve Kahn, Vladimir Kashikhin, Mauricio Lopes,
Miao Yu, John Tompkins, Sasha Zlobin, Vadim Kashikhin

## Slide 16: Current design issue
Need more professional support to design practical channel to see
  Feasibility
  Cost estimate
Need more tests
  High pressure RF cavity
  HS coil test
  6D cooling demonstration

## Slide 17: Conclusion
Cooling in 200 MHz base HCC is as good as 325 MHz one
Feasibility of helical solenoid coil
  Initial & 2nd HCCs look will be ok
  Need more work on final HCC
  Great progress with Fermilab TD & Muons Inc
Practical design of helical RF cavity
  Need to demonstrate high pressure RF cavity with beam!
  Find less expensive and low loss tangent ceramics
  Combine dielectric loaded and and re-entrant cavity to design new RF module
  Some progress with Fermilab TD & Muons Inc
Estimate RF power consumption
  Current design is too premature to see the cost and feasibility
Design cryogenic system
  Force flow LN2 cooling system looks feasible

## Slide 18: Backup slide

## Slide 19: 325 MHz harmonics base HCC
Backup slide
ν = 0.325 GHz
λ = 1.0 – 0.8 m
ν = 0.65 GHz
λ = 0.5 – 0.3 m
ν = 1.3 GHz
λ = 0.3 m
100 % @ z = 0 m
92 % @ z = 40 m
86 % @ z = 49 m
73 % @ z = 129 m
66 % @ z = 219 m
60 % @ z = 303 m
GH2 pressure = 160 atm
60 μm Be RF window
E ~ 27 MV/m
PIC
REMEX
Goal phase space
Study2a